## Slide 1: Micro Switches
Hyoukjun Kwon
Michael Pellauer
Tushar Krishna

## Slide 2: Outline
Microswitch
  Primitive Switching Operations and primitive switches
  Generic Microswitch Approach
Microswitch Network

## Slide 3: Outline
Microswitch
  Primitive Switching Operations and primitive switches
  Generic Microswitch Approach
Microswitch Network

## Slide 4: Primitive Switching Operations
Minimal Switches
Duplicate
Branch
Merge
Distribute Switch
Merge Switch

## Slide 5: Primitive Switches
Distribute Switch
D
OutA
OutB
In
Inv
Inv
OutA
OutB
In
D
OutA
OutB
In
D
OutA
OutB
In
Branch
Duplicate
<Supported Operations>
<Microarchitecture>
Control Registers
Invalid Signals

## Slide 6: Primitive Switches
Merge Switch
M
InA
InB
Out
Arb
InA
InB
Out
Merge
M
InA
InB
Out
<Supported Operations>
<Microarchitecture>
Can use other arbiters
ReqB
ReqA
Grant
Last
Used
2:1 matrix arbiter
Combining primitive switches, we can construct larger switches

## Slide 7: Lookup table
Previous Grant | Req A | Req B | Grant[Output] | Expect
1(pre grant B) | 1 | 1 | 0(grant A) | 0(grant A)
1(pre grant B) | 0 | 1 | 1(grant B) | 1(grant B)
1(pre grant B) | 1 | 0 | 0(grant A) | 0(grant A)
1(pre grant B) | 0 | 0 | 1(grant B) | z(nan)
0(pre grant A) | 1 | 1 | 1(grant B) | 1(grant B)
0(pre grant A) | 0 | 1 | 1(grant B) | 1(grant B)
0(pre grant A) | 1 | 0 | 0(grant A) | 0(grant A)
0(pre grant A) | 0 | 0 | 1(grant B) | z(nan)
ReqB
ReqA
Grant
Last
Used
2:1 matrix arbiter
Grant has no meaning when Req A & Req B are 0 simultaneously
assign o_valid = req_a | req_b

## Slide 8: Combining Primitive Switches Further
Larger General switches
M
D
D
M
Full 2:2 Switch
Full 5:5 Switch
(Mesh Router)
D
D
D
D
D
D
R
R
R
…
East
Local
…
Local
R
R
R
East
…
Do we need fully general switches?
Four Primitive Switches
30 Primitive Switches
Notes: No, traffic is not arbitrary and we have static knowledge about it
Let’s rethink from the basics. We show you how your familiar router can
Trying to make primitive building blocks than a wormhole router, thus allow for static hardware savings
“composable”, but not as primitive.

## Slide 9: Breaking Down Router Boundaries
M
M
M
M
M
M
M
M
M
M
M
M
D
D
D
D
D
D
D
D
D
D
D
D
N
E
S
W
N
E
S
W
D
D
D
L
M
M
M
L
We need a primitive that allows composition and customization at a finer granularity
Buffering should only be added
as a function of physical delay
Notes: Erase -> mention static knowledge about traffic

## Slide 10: Outline
Microswitch
  Primitive Switching Operations and primitive switches
  Generic Microswitch Approach
Microswitch Network

## Slide 11: Introducing Microswitches
Microswitch: A library of 2x2 switches that consist of primitive switches (merge/distribute) in various arrangements
  Also allows pass-through if bandwidth merges not desired
  Buffers can be added as a static parameter
Fine-grained: Allows for large degree of customization
Composable: 2x2 switches naturally express basic traffic flows in two dimensions
M
D
D
Inputs
Outputs

## Slide 12: Microswitch Library
Six 2x2 Switches (Ignoring Rotations)
M
D
D
M
M
D
D
M
D
D
D
M
D
D
Half Distribute
Half Merge
Selective Distribute
(1:2 bus/1:2 tree)
Full Distribute
Full Distribute
and half Merge
Full Merge
(full 2:2 switch/
2:2 crossbar)

## Slide 13: Taxonomy of MicroSwitches
Name | Operation | Operation Direction | Bandwidth (after Op.) | Note
Half-merge Switch | Merge | Single | 1X/1X | Collection Network
Half-Distribute Switch | Distribution | Single | 2X/1X | Distribution Network
Full-merge Switch | Merge | Both | 1X/1X | Full 2x2 Switch
Full-Distribute Switch | Distribution | Both | 2X/2X | 
Selective Distribute Switch | M&D | Both | 1X/1X | 1:2 Bus/Tree
Full-Distribute and Half-Merge Switch | D&M | Half | 1X/2X | 

## Slide 14: Organizing Microswitches
M
D
D
M
M
D
D
M
D
D
D
M
D
D
Half Distribute
Half Merge
Selective Distribute
(1:2 bus/1:2 tree)
Full Distribute
Full Distribute
and half Merge
Full Merge
(full 2:2 switch/
2:2 crossbar)
How can we efficiently construct an array of microswitch to provide desired connectivity?

## Slide 15: Outline
Microswitch
Microarchitecture
  Logical Network Topology
  Microswitch Design
  Microswitch Network Design

## Slide 16: Revisit: Traffic Patterns in DNN accelerators
Pattern | Source | Destination | Need Multicast? | Note
Distribution | GBM | PEs | Yes | 1:Many
Collection | PEs | GBM | No | Many:1
Local | PEs | PEs | No (Mostly) | Many 1:1
We can exploit the static knowledge about traffic to construct minimal network topology

## Slide 17: Network Logical Topology
PE and GBM Placement
GBM0
PE
PE
…
PE
GBM1
GBM0
PE
PE
…
PE
GBM1
GBM0
PE
PE
…
PE
GBM1
Bidirectional flow
GBM0
PE
PE
…
PE
GBM1
Unidirectional flow
Separate Placement
Interleaved Placement
Collection
Distribution

## Slide 18: Network Logical Topology
1D vs 2D
GBM0
PE
PE
…
PE
GBM1
Congestion between GBMs
1D Topology
2D Direct Topology
…
…
GBM1
PE
PE
PE
GBM0
PE
PE
PE
2D Indirect Topology
(Proposed)
Extra links to distribute traffic using pass-through
Overhead?
Less congestion
GBM1
PE
PE
PE
…
…
GBM0
Interleaving Effect
Notes: 2D-edge
Excluded 3D because
Chip is 2D
We have only one source and one destination; it is natural to separate them into two dimensions

## Slide 19: Network Logical Topology
Composable Buffer(GBM)
Composable Buffer(GBM)
Overhead Estimation
N PEs
M GBM Ports
GBM1
PE
PE
PE
…
…
GBM0
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
PE
PE
R
R
R
R
…
R
R
R
M GBM Ports
N PEs
Number of switches: O(NM)
Number of Routers: O(N+M)
>>
?

## Slide 20: Network Topology
Overhead Estimation
We can regard a mesh router(5x5) as an entity of 25 1:1 switches and five 5:1 arbiters.
  (N, E, S, W, and Local)
  x (N, E, S, W, and Local) = 25 switches
We can regard a microswitch(2x2) as an entity of four 1:1 switches and one 2:1 arbiter.
  Distribution: two 1:1 switches
  Reduction : two 1:1 switches + 2:1 arbiter

## Slide 21: Network Topology
Overhead Estimation
Number of GBM Ports = 2
Number of GBM Ports = 4
Number of GBM Ports = 6
Number of GBM Ports = 8
X-axis: Number of PEs
Y-axis: Total Number of 1:1 Switches
Also need to consider…
Output port Arbiter overhead:
-> 25X in mesh
(five 5x1 arbiters vs. 2x1 arbiter)
Other router logics:
- Routing calculation, flow
control, etc.
Future works: Applying hierarchical topology to minimize overhead
Notes: Future works: Combining with hierarchical network topologies to minimize overhead

## Slide 22: Outline
Microswitch
Microarchitecture
  Logical Network Topology
  Microswitch Design
  Microswitch Network Design

## Slide 23: Communication Pattern on Our Topology
Static Knowledge
GBM
PEN-1
PE1
PE0
…
GBM
PEN-1
PE1
PE0
…
Collection
Distribution
PE0
PE1
PE2
Local
Most dataflows repeats the same communication pattern many times
-> Remove routing calculation using coarse-grained circuit switching
Sends the same data to multiple PEs from GBMs
-> Support simultaneous multiple multicasting from GBMs
Many to some communication bound to GBM write bandwidth
-> Provide the same bisection bandwidth with GBM write bandwidth
Because of locality, local traffic in most of efficient dataflow is between adjacent PEs

## Slide 24: Switch Design
Collection Network
GBM
PEN-1
PE1
PE0
…
<Traffic to support>
M
D
In_SW
In_PE
Out_GBM
Out_SW
<Microarchitecture>
Notes: Explain port naming convention.
What is at the end of the direction

## Slide 25: Generic Microswitch Approach
M
D
D
M
M
D
D
M
D
D
D
M
D
D
Half Distribute
Half Merge
Selective Distribute
(1:2 bus/1:2 tree)
Full Distribute
Full Distribute
and half Merge
Full Merge
(full 2:2 switch/
2:2 crossbar)

## Slide 26: Switch Design
Distribution Network
GBM
PEN-1
PE1
PE0
…
Extra Bandwidth for non-blocking Multicast
<Traffic to support>
<Microarchitecture>
Out_SW
Out_PE
In_GBM
In_SW
D
Notes: Explain port naming convention.
=> What is at the end of the direction

## Slide 27: Generic Microswitch Approach
M
D
D
M
M
D
D
M
D
D
D
M
D
D
Half Distribute
Half Merge
Selective Distribute
(1:2 bus/1:2 tree)
Full Distribute
Full Distribute
and half Merge
Full Merge
(full 2:2 switch/
2:2 crossbar)

## Slide 28: Outline
Microswitch
Microarchitecture
  Logical Network Topology
  Microswitch Design
  Microswitch Network Design

## Slide 29: Distribution NoC Design
GBM0
GBM1
PE 0
PE 1
PE 2
PE N-1
…
Non-blocking Multiple Data Transfer
The same
bandwidth with GBMs
Vertical lanes: exclusive for each GBM port
Horizontal lanes: exclusive for each PE
Bandwidth increases

## Slide 30: Distribution NoC Design
…
Operation Examples
Example) [Multiple multicast]
PE 0 and 2 require W0,
PE 0, 1 and K-1 require I3,
PE 1 and 2 require P2,
and PE 2 and K-1 require W2
W0
I3
P2
GBM0
GBM1
W2
PE 0
PE 1
PE 2
PE N-1

## Slide 31: Distribution NoC Design
GBM0
GBM1
PE 0
PE 1
PE 2
PE N-1
…
Features
Non-blocking NoC
Deterministic routing (YX)
Circuit-switching without Ack
  Each source-destination pair is independent
End-to-end Credit-based flow control
  Circuit switching guarantees exclusive routes (no need for flow control between switches)

## Slide 32: Collection NoC Design
…
GBM0
GBM1
PEN-1
PE1
PE0
Collection bandwidth is bound to GBM write bandwidth
Bisection bandwidth: the same as GBM bandwidth

## Slide 33: Collection NoC Design
Features
…
GBM0
GBM1
PEN-1
PE1
PE0
Deterministic routing (XY)
Packing-switching with minimal arbiters
  Merge switches manage 2:1 arbitration
local flow control: Switch-to-switch on-off flow control